## Slide 1: Putting It All Together with xLights
Matt Brown
(dowdybrown on DIYLA & DIYC)

## Slide 2: Purpose Of This Class
Learn the capabilities of xLights
Learn how to install and configure xLights
Learn how to apply the capabilities of xLights to your Show

## Slide 3: xLights Capabilities
Show scheduler
Tester
Sequence Converter

## Slide 4: Benefits
Support for a wide variety of lighting controllers and networks
Reliable, flexible scheduling. Playlists can be scripted to run in any order and can respond to input from external sources.
Robust testing module for both traditional and RGB lights, including Smart Strings
Runs on Windows, Mac, and Linux

## Slide 5: USB Driver
If you are using any type of USB dongle, ensure you have the FTDI VCP drivers installed.
If you have successfully used an LOR or Lynx dongle on your system, you already have the right driver installed.
This step is only required for Windows and Mac systems. FTDI drivers are already built in to most Linux distributions.
Drivers can be found here: http://www.ftdichip.com/FTDrivers.htm

## Slide 6: Downloading xLights
Ready to run versions of xLights for Windows and Mac can be downloaded from SourceForge:
  http://sourceforge.net/projects/xlights/files/
After downloading, just double-click on the file
Linux users need to compile xLights. Instructions are here:
  http://xlights.svn.sourceforge.net/viewvc/xlights/trunk/ToolConfig.txt?view=markup

## Slide 7: Show Directory
xLights expects you to organize all of your sequence files and associated audio or video files into a single directory.
You can have a directory called "TestSequences" with some sequences you are testing.
For your 2012 show, you can have a directory called "2012 Show".
Don't bother starting xLights until you have this directory created. But once you do, fire up xLights (xMenu module).

## Slide 8: Main Menu (xMenu)
Currently selected show directory
Change show directory
Define your lighting networks
Define schedule, run schedule, and test lights
Convert sequences from one format to another

## Slide 9: Lighting Networks
The next thing you will need to do is define your lighting network(s).
xLights ignores most of the information about your lighting network contained in your LOR or Vixen sequence. Thus this step is very important.

## Slide 10: Lighting Networks
Click on the "Network Setup" button to bring up the network definition grid.
Add a row for each network or universe used in your display.
If you have 1 USB dongle, then you just need one row in your table.
if you have a larger display with more than one network, xLights can drive a mixture of network types (DMX, LOR, Renard, Pixelnet, and E1.31 can be intermixed).

## Slide 11: Lighting Networks

## Slide 12: Lighting Networks - EtherDongle

## Slide 13: xScheduler
Create Playlist(s)
Create schedule
run schedule
Or…
test lights

## Slide 14: Create Playlist
#1: Click “+” button to add a new playlist
#3: Click OK
#4: Your new playlist will be added as a new tab
#2: Enter the name for your new playlist

## Slide 15: Configure Playlist
#1: Click the checkbox for the type of files you want included in your playlist
#3: Adjust playlist order by clicking on a file name then clicking the up or down buttons
#2: Select a file name in the box on the left, then click the “>” button to move it into the playlist. Repeat as necessary.
#4: Click Save icon

## Slide 16: Other Playlist Options
Delete the current playlist
Set a delay after the item plays by selecting the item, then click the “Set Delay” button
If you sequence to movies instead of music, selecting “Movie Mode” for playback will show the movies full screen.
Get help
Add all items to playlist
Remove item from playlist
Remove all items from playlist
Play the selected item in the playlist
See how sequence channels are mapped to physical channels

## Slide 17: Create Schedule
First thing to do is set the show’s start and end dates

## Slide 18: Create Schedule
Once dates are set, one or more playlists can be scheduled each day

## Slide 19: Update Schedule
Mass updates to the schedule are possible by selecting multiple playlists using Ctrl-Click or Shift-Click, then selecting Update or Delete selected items. Selected date headings are ignored.

## Slide 20: Run Schedule
The schedule will only run when the “Run Schedule” checkbox is checked. The state of this checkbox is remembered between program invocations.

## Slide 21: Testing Your Lights
Enter the testing module by clicking on the Test icon on the toolbar.

## Slide 22: Standard Tests
Select multiple channels by using shift-click or Ctrl-click. Then click the checkbox of any of the selected channels to activate all selections.
When finished testing, turn all lights off, then click close

## Slide 23: RGB Tests
These tests treat lights in groups of 3.

## Slide 24: RGB Cycle Tests
These tests treat lights in groups of 3. Every group of 3 gets the same color.

## Slide 25: xConverter
Convert sequences from one format to another

## Slide 26: xConverter Formats
All output formats use 50 msec timing
Input | Outpus |  | 
 | xLights Format (.XSEQ) | Lynx Conductor (.SEQ) | Vixen 2.1 (.VIX)
LOR Music (.LMS) |  |  | 
LOR Animation (.LAS) |  |  | 
Vixen 2.1 (.VIX) |  |  | 

## Slide 27: xConverter Operations
#1: Select files to be converted
#2: List of selected files is displayed here
#3: Choose output format
#4: Select if you want all lights forced off at the end of the sequence
#5: Start the conversion
#6: Status messages will display here

## Slide 28: Tip #1
Do not play back Vixen or xseq files over an LOR network
  This will work ok for 16-32 channels, but is not recommended
  Use LOR controllers in DMX mode instead
  LOR sequences can be efficiently played back to any type of network

## Slide 29: Tip #2
If you have a lot of channels, then use xConverter to convert your sequences to xseq format.
Xseq files load/start much faster